Method Statement and Risk Assessment for General Stone Masonry including Dry Stone Walling.

Contents of Method Statement

1.	Scope and method of work

2. 	Project organization for health and safety control

3.	Health and safety risk control / Assessment

4.	Workplace access and egress

5.	Workplace lighting

6.	Plant and equipment

7.	Personnel training certification

8.	Hazardous materials and substances

9.	Waste management

10.   Special control measures

11.	Contact Numbers

12.	 Communication of Method Statement

1. Scope and method of work

The method statement relates to the safe way in which T.Moore Stone Masons will conduct Stone Masonry work in a safe and proper manner.

Method of Work

Stages of the work we will be undertaking

- Arrival on site.

- Get to place of work. The area will be assessed to ensure a safe route is possible. Vehicles will be parked in the correct location and where required High Visibility clothing will be worn at all times.

- Steel toe capped boots will be worn at all times.

- Any equipment and stone brought onto site will be unloaded in a safe area and near the area of work.

- An area for waste will be established and any waste materials generated will be kept in this area. Waste materials will be removed off site by Scott Stone stone masons unless it is agreed with the client that their waste facilities can be used.

- Gloves will be worn when handling and transporting any materials.

- Foundations / footings may need to be dug. This will either be done manually by spade or for large areas by mechanical digger. Only suitably trained operatives will use mechanical equipment.

- Stones will be lifted into the correct position. Heavy or awkward shaped stones will be lifted by two people.

- Stones may require some cutting. In which case a stihl saw is used. All operatives will be suitably trained in using a stihl saw safely. Dust mask and eye protection will be worn when using the saw.

- The job may require cement to be mixed. In which case gloves will be worn. The cement will either be mixed manually or by machine. If a machine is used then the operator will be suitably trained to operate it safely.

- Once the job is completed all waste will be removed from site

- Any issues that arise during the job will be discussed with the client before continuing.

- No work will be started if there is a risk to the health and safety of ant Scott Stone stone masons staff or subcontractors or any other contractors or visitors  who maybe on site.

2. Project Organisation for Health and Safety Control

All Scott Stone stone masons staff will be fully trained in the work they are doing. They can contact Nicky Scott at any time.

| Title | Name | Contact No |
| --- | --- | --- |
| Stone Masons and Company owner | Nicky Scott | 0772 4407 148 |
| Stone Mason | Joe Bloggs | 12345678910 |

All stone masonry work will be overseen by Nicky Scott. All staff report to him and are instructed to report any Health and Safety issues immediately.

All staff and subcontractors will receive a copy of this method statement and will work in accordance to it.

3. Health and Safety risks and controls / Assessment

| Task | Building and repair of dry stone walling and general stone masonry | Description of task and frequency | Scott Stone stone masons will turn up to site and perform stone masonry work, such as dry stone walling. This is the core business of Scott Stone stone masons and all employees are well experienced in this task which they do on a daily basis. |
| --- | --- | --- | --- |
| Assessment covering | Scott Stone stone masons and all their employees and sub contractors. |  |  |

| Task | Describe Hazard and possible Harm | Describe who might be harmed | List ALL existing controls | Risk Rating Likelihood X consequence | Further Action Required |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | L | C | RR |  |
| Lifting / Transporting stones | Failure to lift stones correctly could result in serious muscular damage or impact damage from dropping the stones | All Scott Stone stone masons staff | ■ Wherever possible stones are lifted by mechanical means. ■ Heavy stones will always be lifted by two people. ■ All staff have General Manual Handling Training ■ All staff will wear suitable PPE to include steel toe capped boots | 2 | 3 | 6 | .None |
| Lifting /Transporting Stones | Sharp edges and awkward shaped stones could cause cuts to hands | All Scott Stone stone masons staff | ■ Gloves will be worn whilst lifting and transporting stones | 1 | 2 | 2 | None |
| Moving around site, often uneven/ wet ground | Uneven or wet ground could easily cause slips and trips. | All Scott Stone stone masons staff | ■ All staff are responsible for ensuring they have safe access to the walling area. ■ Correct footwear will be worn at all times with good grip. Worn out boots will be replaced as required ■ Area will be kept as clear as possible with designated area for stacked stones. | 1 | 3 | 3 | None |
| Dressing Stone | Chips from stones could get into the eyes or hit the face and cause cuts. Stone dust could cause inhalation problems | All Scott Stone stone masons staff | ■ safety glasses will be worn whilst dressing stone ■ Dust mask will be worn when cutting stone. | 1 | 2 | 2 | None |

Scoring System. Likelihood 1=Highly Unlikely through to 5=Very Likely to happen.   Consequence 1= Very Minor accident requiring no first aid through to 5= Fatal Accident

RR = 1-5 Acceptable (no further action),   6-9  Ok to work but try to improve 10-16 Improve before starting work, 20 – 25 DO NOT undertake any work until extra controls put into place.

| Task | Describe Hazard and possible Harm | Describe who might be harmed | List ALL existing controls | Risk Rating Likelihood X consequence | Further Action Required |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | L | C | RR |  |
| Working in adverse weather conditions. | The sun could cause sunburn /skin cancer if working for long periods outside. Also the cold and wet weather could serious health issues such as hyperthermia. | All Scott Stone stone masons staff | ■ All staff will take frequent rest breaks in adverse weather. Protection from the sun /rain / cold can be obtained by sitting in the van/vehicle. ■ On hot sunny days sun hats/caps will be worn and sun cream will be applied to protect the skin. ■ In cold or wet weather correct protective PPE will be worn at all times. | 1 2 | 5 2 | 5 4 | None |
| Dealing with Accidents | Failure to get emergency help or issue first aid could make any injury worse. | All Scott Stone stone masons staff | ■ All staff carry a mobile phone to get help if required ■ First aid kit carried in all vans | 1 | 5 | 5 | None |
| Using Machinery | Stone masonry does not require much use of powered machinery however stihl saws and cement mixers maybe used. These can cause serious cuts or entanglement injuries. | All Scott Stone stone masons staff | ■ Any staff who operate the machinery will have the correct training for such machinery. ■ If the machinery is broken or damaged in any way it will not be used. ■ PPE will be worn at all times ■ Replacement blades for stone cutters will be replaced as and when required and only by trained staff. | 1 | 4 | 4 | None |
| Use of chemicals | Cement, Lime and petrol are all handled and used. These can cause contact burns and in the case of petrol is highly flammable. | All Scott Stone stone masons staff other contractors or people on site. | ■ A Chemical assessment will be completed for each chemical used. ■ Overalls and gloves will be used when handling cement and lime. ■ All chemicals will be stored correctly. Petrol will be stored in a metal storage can designed to hold petrol. | 2 | 3 | 6 | None |

Scoring System. Likelihood 1=Highly Unlikely through to 5=Very Likely to happen.   Consequence 1= Very Minor accident requiring no first aid through to 5= Fatal Accident

RR = 1-5 Acceptable (no further action),   6-9  Ok to work but try to improve 10-16 Improve before starting work, 20 – 25 DO NOT undertake any work until extra controls put into place

4. Workplace access and egress

Access and egress to site will be provided by the customer.

Access around egress around the site  will be assessed before starting work to ensure it is safe.

5. Workplace Lighting

Generally work is outside and natural light it suitable to do the task.

6. Plant Equipment

PPE

All PPE provided by Scott Stone stone masons will conform with the relevant EN number and be fit for purpose.

Electrical Equipment

It is not anticipated electrical equipment will be required for this work.

Lifting Equipment

It is not anticipated that the job will require any form of load bearing equipment.

General Equipment

The following Equipment will be used as part of the job

- Cement Mixer

- Stihl Saw

7. Personnel Training Certification

All Scott Stone stone masons staff have CSCS cards

All staff have had manual handling instruction.

8. Hazardous Material and Substances

Three hazards substances maybe used during the work. A chemical risk assessment has been completed for each one.

Cement and lime

Gloves and protective clothing will be worn at all times when handling when cement

Petrol

This will be stored in suitable metal containers. Petrol is only used to power equipment listed above.

9. Waste Management

All waste generated will be removed off site by Scott Stone stone masons unless it is agreed with the client that there waste disposal maybe used.

10. Special Control Measures

It is not anticipated any special control measures are required.

11.  Contact Details

Emergency Services

Fire/ Ambulance – 		999 or 112 from mobile or landline

| Company Owner | Nicky Scott | 0772 4407 148 |
| --- | --- | --- |
| Stone Mason | Joe Bloggs | 12345678910 |

12. Communication of Method Statement

Details below show that person involved with of the method statement and understand their responsibilities within this document.

The method statement has been talked through with Scott Stone stone masons staff and subcontractors.

All employees or sub contractors who do not work to this method statement when doing work on behalf of Scott Stone stone masons will be removed from site.

| Employee Name (print) | Signature | Date |
| --- | --- | --- |